## Slide 1: TCP Performance and Diagnostics: Optimizing for High Performance Networks
Chris Rapier
Pittsburgh Supercomputing Center rapier@psc.edu CANS
16 September 2014

## Slide 2: The Scientific Workflow and HPNs
Collaboration requires optimized reliable networks
  The scientific work flow often depends on the transfer of massive data sets
    E.g. 1000 Genomes Public Data set is 232TB
  Data sets will continue to grow in size
  Transferring those data sets to and from compute nodes is critical
  Failures in the network can delay the workflow by days if not longer
Notes: Scientific research has always relied on reliable access to data. In a growing number of fields, from genomics to literary analysis, the corpus of data has not only been growing exponentially, but the physical location of the data is often geographically dispersed over vast distances. As such, it is often a requirement that researchers have access to high performance networks in order to migrate data to compute and visualization resources. In order to meet this requirement network engineers have to consider the network at every layer – the physical path, the nature of IP transport, the demands and restrictions of the protocol, potential inefficiencies in the application, and even the I/O constraints of the local compute infrastructure (from firewalls to rotating media speed). This is further complicated by the fact that the primary users of the network may not have the proper background to provide required information to troubleshooters when a problem is encountered.

## Slide 3: The Bandwidth Delay Product
Bandwidth delay product
  BW * RTT = BDP
  ‘carrying’ capacity of the path between endpoints
    Think of it like the water in a hose between the faucet and the nozzle.
  Example: 10Gb path with 250ms RTT
    1280MB/s * .250 s = 320 MB in transit between endpoints.
  In order to maximize utilization you need to keep the path full.
Notes: It’s important to start with the basics. While the assumption can be made that everyone knows about BDP, ACK behaviour, buffer sizes, and loss rates these are often overlooked by enough people to make it worth reviewing. This is especially true considering how much of an impact these characteristics have on performance.
The first definition of a long fat network (LFN) is described in RFC 1072 as a path where the bandwidth delay product exceeded 12500B. Why? Because when the BDP started to exceed that number TCP started to have performance problems. Advances in congestion control algorithms have significantly increased the amount of outstanding data that TCP can comfortably deal with. As such, the dividing line between LFN and non-LFN networks is not necessarily quantifiable as it has become a moving target. Generally speaking an LFN should be thought of as any path with a bandwidth delay product (BDP) sufficiently large enough to have a notable impact on overall performance.
High performance networks (HPN) may or may not be LFNs depending on the path characteristics. For example, an infiniband infrastructure within a data center is a high performance network but doesn’t have the BDP associated with a LFN. Generally speaking HPNs are carrier and research grade network infrastructure and should be thought of as a distinct class from consumer level networks (even though the HPN of 5 years ago is consumer grade now). Understanding BDP is critical in order to achieve network optimization for high throughput applications. It’s imperative that the receive side TCP buffer is close to the BDP of the path. If the receive buffer is undersized significant performance penalties may be imposed.

## Slide 4: ACKs and Receive Buffers
TCP is a reliable and congestion avoidant protocol because of ACKs
  Reliable:
    Used to inform the sender that the data arrived and ready to receive new data.
    Duplicate acks indicates missing data
  Congestion avoidant: Receive buffer & window
    Max receive window size determined by receive buffer
      Modulated by the window scaling option
    Tells the sender exactly how much data it can send at one time.
    The window size increases each RTT until the window is full or congestion is encountered.
Notes: ACKs are multipurpose tools in TCP. Not only do they confirm that the data has been received they also inform the sender how much more data the receiver can accept. Every packet sent includes a sequence number. The initial sequence number is randomly assigned but increments by the amount of the payload in each datagram sent. For example, an initial sequence number might be 39 and the payload is 700 bytes in size. When the receiver gets this packet it will generate an ACK with an acknowledgement number of 739. This indicates to the sender that it received all 700 bytes of the payload. As the number of packet sent in each RTT increases the sequence number of the ACK will be the total of all the packet payloads received. If the receiver gets a packet with an out of order sequence number it will ack the *last* sequential sequence number. If the senders get 3 duplicate ACKs in a row it will retransmit the data. How much data is resent depends on the use of SACK vs ACK. SACK will only retransmit the missing data as opposed to all of the data since the last received ACK number. TCP has two main mechanisms to indicate that the sender should delay sending more data – the receive buffer and the receive window. The buffer and the window are related in that the maximum size of the window is determined by the buffer. The window exists as a stack mechanism - specifically in that while it is informed by the receive buffer it has it’s own mechanism to determine how much space to advertise. This mechanism, known as congestion control, typically relies on an additive increase and multiplicative decrease (AIMD) algorithm. Different algorithms tweak the rate of addition and decrease in order to meet design criteria (friendliness, recovery speed, etc). The receive buffer is driven by how quickly the host system and associated application can draw data off of the incoming data buffer. They have overlapping influence such that the minimum of the two values dictate how much outstanding data is allowed on the path. In most real world situation the value of the receive buffer is of primary importance. This isn’t to say that a misconfigured system or middle box might not artificially limit the receive window (usually through a rewritten window scale) but in practice the receive buffer tends to be more problematic in HPN environments.

## Slide 5: How BDP, Buffers, and ACKs relate
The goal is to have as much data in flight as possible.
  The physical maximum is the BDP.
  The sender moderates the amount of data being sent based on the ACKs received.
  The maximum allowed in transit before having to ACK is the minimum of the window and buffer
Ergo: The receive buffer should always be as close to the BDP as possible.
  This also applies to the sender’s send window
Notes: Imagine that you are trying to water a garden with a watering can you are filling from a hose. A friend of yours is controlling the faucet (the sender) and you (the receiver) tells him to turn on the hose. Initially you don’t know how much water (data) will come out of the hose so you tell him to open the faucet a small amount (a packet). After a moment he turns off the faucet and waits for you to tell him to start it up again (ACK). Each time you do he opens up the faucet more and more (slow start). When your watering can is full you tell him to turn off the hose so you can empty it. If you have a tiny watering can you’ll spend most of your time without the faucet being opened. If you have a large watering can the faucet is fully open for much longer periods of time before you need to tell him to wait. Ideally you want a watering can (receive buffer) that holds as much water as there is water in the hose between the faucet and the nozzle (the BDP). The internet really is a series of tubes.

## Slide 6: Automatic Receive Buffer Tuning
No need to tune buffers by hand (sort of)
  This used to be a requirement
    Automatic receive buffer tuning developed at PSC and now part of every major operating system
  The default values are *undersized* for large TCP flows on HPN though
    Usually around 4MB
      BWmax = RcvBuf / RTT
        4MB on a 250ms path = 128Mb/s
    For large TCP flows the maximum receive buffer *must* be increased. A lot.
      Don’t forget the send buffer either!
Notes: There are a number of guides for maximizing TCP performance through the adjustment of system control parameters on the host. http://www.psc.edu/index.php/networking/641-tcp-tune is a good place to start but the suggested values are still undersized for very long very fat networks (VLVFN) such as a 10Gb link between NYC, NY and Beijing. http://fasterdata.es.net/host-tuning/linux/ has more current values. Nothing is that simple though. While a 10Gb connection with 250ms RTT requires a 320MB buffer it’s unlikely that any transfer would have all of the 10Gb/s path to itself. This means it will encounter congestion (or I/O contention on the hosts). While it is possible to set a receive buffer to 320MB there is little practical need for it on a shared link. Generally speaking it makes more sense to set the maximum receive buffer to a value that corresponds to between 32MB and 64MB on LFNs.

## Slide 7: Back to ACKs
ACKs are used to indicate loss
  So how much loss can a given path tolerate?
    Rate <= (MSS/RTT)*(1 / sqrt{p})
  To maintain a single 10Gb/s TCP flow
    9K packets: loss rate of less than 1:10^9
    1500B packets: loss rate of less that 1:10^10
  Excessive loss can drop a connection back into slow start
    Recovery can take a *very* long time in high RTT environments
Notes: The Mathis Formula can be found in http://www.psc.edu/networking/papers/model_ccr97.ps and an updated, more accurate formula can be found in http://www.acm.org/sigcomm/sigcomm98/tp/paper25.pdf but that formula is significantly more complicated. As you can see from the acceptable loss rate packet size is an important consideration. The primary reason being that 6 1500 byte packets are needed for each 9k packet. Reducing the number of packets reduces the probability of loss. Fewer packets also mean less compute power required to process the headers. Additional, 9K packets have less overhead (40 bytes as opposed to 240bytes). Slow start increases the number of segments per RTT exponentially 1, 2, 4, 8, etc. Congestion- avoidance increases atomically per RTT 1, 2, 3, 4… Dropping into slow start and congestion avoidance can impose a huge penalty and the amount of time it takes to recover is directly dependent on the bandwidth and RTT. The higher either are the more time it will take to recover.

## Slide 8: How to avoid loss
You can’t. Loss is unavoidable.
  You can learn to live with it though
  More advanced congestion control algorithms make a difference
    Stop using Reno (especially if you have older installations)
    Default for Linux is now CUBIC
      Other algorithms may be more effective (HTCP, Fast TCP, etc) so be sure to test them on your network.
  If using Linux update your kernel
    Proportional Rate Reduction ensures the window size is set as close as possible to SSThresh after loss. In a lossy network PRR provides a 10% improvement in average latency and recovery timeout reduced by 5%. That’s a win.
Notes: Being that TCP is becomes more sensitive to loss as bandwidth and RTT increases minimizing loss and congestion events is critical. However, packet loss is an unavoidable part of any network. No matter how well designed it is a statistical inevitability that loss will be seen given a large enough number of TCP packets. However, excessive loss can be engineered out of a network and, at the same time, the impact of any existing loss can be minimized through the use of more modern TCP stacks and protocols. What counts as current? To have CUBIC enabled by default you should be using at least 2.6.19 which shouldn’t be a problem as that kernel was released around 2007. However, CUBIC is not your only choice in terms of congestion control algorithms. Different algorithms have different qualities that may or may not be beneficial depending on the path characteristics. It’s not a bad idea to compare a standardized transfer using the different algorithms to determine which might be best for your needs. Hat being said, CUBIC is reasonable choice. Proportional Rate Reduction is also going to be beneficial when one experiences a burst of losses. If too many losses are experienced in a short period of time the effective congestion window will fall below ssthresh. PRR works by trying to limit the reduction in window size so as to keep in within the bounds of the congestion control algorithm but above ssthresh. This was introduced in 3.2.
Controlled Delay, a mechanism to fight against BufferBloat was introduced in 3.5. This revision also saw the introduction of TCP Early Retransmit which, under some circumstances allows the stack to avoid the Retransmisison Time Out (RTO) which can be costly in some environments. In other words, if you aren’t actively managing every aspect of your kernel’s TCP stack (including applying patches to older versions) upgrading to more recent kernels is often in an organization’s best interest. Obviously, the kernel has to be able to support other required functionality (drivers, modules, etc)

## Slide 9: Other Options
Don’t use a single high bandwidth stream
  Multiple parallel streams provide insurance against loss without extreme tuning
    A 1Gb/s connection is roughly 100 times less sensitive to loss.
    In the event of loss recovery is significantly faster
Use alternative protocols
  UDP-based Data Transfer Protocol
    A reliable UDP protocol designed for use in high performance environments.
    Optional in GridFTP
Notes: With parallel streams you essentially split the potential impact of loss across multiple less sensitive streams. For example, if one has 5 x 1 Gb/s streams the maximum acceptable loss rate per stream is approximately 1:10x7 packets. If any individual stream experiences a loss event it is, in all likelihood, independent of the other streams. So while one of the five streams may enter slow start the others may not be similarly effected – in effect 80% of your throughput won’t be impacted by a loss on one of the component streams. On the other hand, a single 5Gb/s stream has a maximum acceptable loss rate of approximately 1:10^9 packets. The chance of encountering performance impacting loss is 100 times more likely and reentering slow start, since it’s a single stream, will have a significantly higher impact on throughput. In essence, multiple streams allows one to spread the risk of loss over multiple more robust streams.
UDT is quite well suited for a bulk data transfers over high speed networks because it avoids some of the problems associated with TCP in LFNs. Through the use of rate based flow control (controlling interpacket timing) along with novel approaches to AIMD during congestion, and a more aggressive approach to scaling up to the network limits UDT can be much more efficient that TCP. So why isn’t everyone using it? A lot of ‘WAN Accelerator’ services actually are using UDT. Additionally it’s also an option in GridFTP to make use of UDT. An excellent paper on UDT can be found at http://www.sciencedirect.com/science/article/pii/S1389128606003057

## Slide 10: The Impact of IPv6 on Performance
IPv6 is part of the HPN environment
Fortunately, it should have little impact on network performance:
  Assuming that your average packet size is more than 256 bytes.
    IPv6 increases the header size to 60 bytes. In a 9k packet this is 0.66% of the datagram as opposed to 4% in IPv4.
    As packet sizes decrease it has more impact but not until the 256 byte threshold.
  And that the path is IPv6 end to end
  And, of course, application performance is dependent on the underlying code.
    Mostly a DNS issue though
  NB: It doesn’t fix any of the problems with TCP
Notes: The impact of IPv6 is largely going to be determined by two factors. The ability of the network hardware to effectively handle IPv6 and the size of the packets. Most router and switch hardware being used in current HPN environments handle IPv6 as efficiently as IPv4. As IPv6 adds an additional 20 bytes to the header there is greater overhead than you’d see with IPv4. A literature search indicates that one would only see a statistically significant impact when the average packet size is under 256 bytes (when compared to IPv4 on the same path). Some consideration may need to be taken in highly interactive applications that rely on small packets but large flows should not be affected. A Cisco White Paper from 2007 explored the impact on several platforms and published the results here http://www.cisco.com/web/strategy/docs/gov/IPv6perf_wp1f.pdf
This is not to say that no one has experienced a problem with IPv6 vs IPv4. On dual stack machines DNS responsiveness can be degraded depending on the lookup order of ipv6 vs ipv4. Additionally, if the ipv6 path is not fully compliant users may experience increased latency due to encapsulation and de-encapsulation at each ipv4 tunnel. However, for most network tasks on scientific high performance networks the impact should be minimal. Lastly, IPv6 exists on a lower layer of the OSI model than TCP. As such, it does not and cannot address any of the issues that occur as part and parcel of TCP. The primary goal of IPv6 is to address the limitations of IPv4 and not any of the protocols that ride on top of the IP layer. Changes to layer 3 can impact layer 4 but it’s not the goal.

## Slide 11: Infrastructure Considerations
Firewalls, Deep Packet Inspection, and other middleboxes can destroy performance
  Use a Science DMZ if at all possible
You have to know what is happening
  Not just in your network but along the path as a whole
  Internal: SNMP, NetFlow, logs, Web10G
  External: perfSonar is a key tool
    limited to synthetic benchmarks within the infrastructure
Notes: A science DMZ is, for all intents and purposes, a requirement for an efficient scientific workflow in collaborative environments. Essentially a Science DMZ is a secure subnetwork that does *not* pass through a stateful firewall and is tuned for high performance networking. The goal is to create a fast path for data into the local infrastructure without exposing sensitive infrastructure. Once data enters the DMZ it would pass through local firewalls to the compute resources.
The fact that perfSonar engages in active testing has two implications. The first is that the results can only tell you about the health of the network path between the perfSonar hosts and only in terms of how well they respond to perfSonar tests. It’s an important tool but it’s not a real world test. Second, regularly scheduled tests can and *will* interfere with any other traffic on the network during test periods. How impactful this interference is depends largely the average amount of traffic seen on that path. In other words – having a bwctl test scheduled every four hours on a highly used path is probably a bad idea. That being said, perfSonar deployment should be taken as a given.

## Slide 12: Metrics on the Stack
Web10G!
  Joint project between PSC and Google
  Brings 127 different TCP metrics out of the kernel and to the user (RFC 4898)
  Metrics are provided on a per connection basis
    Detailed look at how the application interacts with the network in real time
    Applications can be easily instrumented or 3rd party monitor can report on all network applications
  Passive monitoring of real world applications
  Foundation for new tools
Notes: Web10G is a follow on project to Web100. Web100 also provided a large number of TCP measurements to the user. However, It never met it’s final goal of inclusion in the Linux kernel mainline. This was primarily due to overhead caused writing the metrics to the /proc filesystem. It simply wasn’t fat enough to be used on production servers. However, Web100 did give the computing world receive buffer autotuning which ended up being a prerequisite to the effective roll out of high speed networking to commodity and home users. Web100 also formed the basis of a number of network diagnostic tools like NPAD and NDT. Web10G is, essentially, a rewrite of Web100 from the ground up – both to make it RFC 4898 compliant and remove the /proc bottleneck by switching to netlink for bringing the metrics out of kernel space.

## Slide 13: Web10G: Insight Project
Notes: Insight is an application that hooks into a local hosts Web10G metrics by way of a websocket server. The goal is to present the user with a visual weather map of their own connections with the ability to report on failing connections to a NOC automatically. The basic usage scenario assumes that a researcher is transferring data sets to or from their own system. The enable the local insight listener and then navigate to a webpage hosted by their NOC that provides the user interface and control mechanisms for the local listener. By default common user connections (HTTP, IMAP, POP, etc) are filtered so it only shows the network connections of most interest in terms of scientific workflow. The user then has a visual representation of the health of their transfer based on information such as throughput, retransmits, congestion events, and so forth. If the user feels that the connection is not performing adequately they can chose that the NOC receive snapshots of the connection every so often (as defined by the NOC). The NOC would then have a longitudinal record of the metrics of the actual connection in question. With this information a network engineer should be able to achieve a deeper understanding of why that connection is failing in context of the user. Of course, this does depend on the user having a Web10G enabled kernel. This should not be as much of a problem once Web10G is adopted by Linux mainline. Later versions of Insight will have the ability to monitor 3rd party transfers (GridFTP) by having the client reside directly on the transfer hosts in the Science DMZ.

## Slide 14: The limits of metrics
Metrics are only the beginning, not the goal
  Data doesn’t mean anything if you can’t make sense of it
    The more metrics you have the more difficult it can be to recognize the important ones.
  Heuristic approaches to the identification of poorly performing flows is a hard problem
    If you don’t know the initial characteristics of the path you cannot absolutely determine if you are on a bad 1Gb/s connect or a great DSL line.
    It’s much easier for a path where the initial conditions are known
      Eg. VLANs created via SDN for single use
With the right heuristics what could we do?
  And do we want to do it?
Notes: Web10G can provide a veritable flood of metrics (127 per connection at millisecond resolution). The problem is that engineers (and researchers) are often at a loss of how to make use of these metrics once it moves past bandwidth and retransmits. When presented with more than a hundred different metrics it’s human nature to simply disregard unfamiliar ones. As such, it’s likely going to be very important to have an algorithmic method to process the incoming metrics based on the relationships between them and over time.
For a very long time network researchers have been gathering measurements and metrics. Often times these are basic measurements used to determine aggregate usage of a network path, RTT, failure rates, and the like. These are of use in that they determine when a path is saturated or may be experiencing persistent problems. However, after a lot of work the community has essentially determined that we simply can’t use those metrics to heuristically determine the health of any individual connection along that path. The reason for this is that it’s almost impossible to know what the initial conditions actually are. For example, a 1 failing 1 Gb/s connection can look very similar to a relatively healthy DSL link (think about the Mathis equation in terms of sensitivity to packet loss). Basically without the initial conditions there are too many unknowns to solve for. However, with SDN we now have the ability to create VLANs with known initial conditions (BW and RTT). With this information in hand we can use gathered metrics to determine the health of a TCP connection in near real time (dependent on the polling interval of the metric). The question is what should happen once a poorly performing connection is identified? With dynamic networking like SDN it would be possible to automatically build a new path between the hosts. However, engineers often express deep discomfort with this idea.

## Slide 15: Networking and Researchers
The users depend on us to inform them of best practices
  Provide them with the tools they need
    HPN-SSH
    Science DMZs
    GridFTP
    Responsive NOCs and NOC tools to reduce turnaround
  Educate users about how to file a trouble ticket
    Turn around on collecting initial information can take days – anything you can do to reduce this delay helps
  Educate your staff on how to work with users
Notes: Networking, even high performance networking, has become a utility service like electricity or water. We don’t expect every person that plugs in a toaster to be an electrician and we shouldn’t expect network users to be network engineers either. It is the job of the network support staff to make networking services as transparent as possible to the researchers. The first step is to educate the researcher about the tools available to them and providing instruction on how to use those tools. A case in point is the use of SSH (SCP or rsync) for file transfers. It’s still relatively common for researchers to transfer large data sets using a default installation of SSH. They’ve used it before, they know how it works, and they are comfortable with it. However, it’s slow on LFNs because of an undersized internal flow control buffer. Admins should make sure that HPN-SSH is available for their use – it’s significantly faster, provides a method for a non-encrypted data stream after an encrypted authentication, has a threaded cipher for encrypted transfers and so forth. Likewise, admins should make sure that GridFTP servers are on well connected properly configured host with adequate fast media. Importantly, you should encourage the use of GridFTP and other advanced transport services whenever possible. Invariably problems will arise. What is critical, in terms of the scientific workflow, is to address the problems as quickly as possible. Often this means collecting information of varying levels of detail from the users. NOCs and engineers must have a base level of information to start the diagnosis. Now, this information may be as basic as the expected versus observed behaviour or a traceroute. Unfortunately this is often where significant delays are encountered as emails are sent back and forth between the NOC and the user. It’s not uncommon for it to take well more than a day to gather the most basic information. If anything more complicated than a traceroute is required (say a tcpdump, Iperf run, etc) it may take more than a week assuming that it is possible at all. As such it’s important for the front line support staff to know how to speak to the users and be able to quickly triage problems. Staff should always seek to eliminate the basic potential problems first – undersized receive buffer, congestion on the path, misconfigured application, firewall problems, etc. Only after the basics have been eliminated should you move on to less likely sources of trouble. This is akin to have a help desk operator asking you if the computer is plugged in – it probably is but if it isn’t you’ll spend hours on a something that should have been a 30 second fix.

## Slide 16: HPN-SSH and GridFTP
GridFTP
  An FTP like file transfer tool built with HPC needs in mind
    Supports 3rd party transfers.
    Well Supported
    Flexible
    Striped transfers using multiple TCP connections
    Can be hard to install, configure, and maintain
HPN-SSH
  Set of patches to OpenSSH that dramatically improves performance
    Lightweight and familiar to most users
    As much as two orders of magnitude faster than OpenSSH
    Multithreaded AES-CTR cipher
    Optional switch to NULL cipher post auth to decrease CPU load
Notes: There are two major tools used for transferring datasets in an HPN environment; GridFTP and HPN-SSH. GridFTP is widely used and well supported in the HPC/HPN community with almost every major research center supporting at least one GridFTP node. One of the major advantages of GridFTP is the support for 3rd party transfers – a user can tell two remote GridFTP nodes to transfer data without having to issue the command directly on the nodes in question. This is a major advantage in a scheduled job environment. It’s also very secure and built with performance in mind. The problem with GridFTP is that it requires a significant investment of time and resources to install and properly maintain. The build process can be difficult and configuration is, at times confusing. These considerations often make it unfeasible for smaller institutions and invariably outside of the domain of a single researcher trying to get their data to a storage node. Many researchers often resort to using SCP and SSH (either on their own or as the transport layer in rsync). However, the most widely used implementation of SSH, OpenSSH, is not built with high performance in mind. The problem stems from the fact that SSH is a multiplexed protocol. You can have multiple data channels existing inside of a single TCP connection. This requires the use of a flow control mechanism which, in the case of OpenSSH is implemented as a receive buffer. The end result is the effective receive buffer of the TCP connection ends up being the minimum of the SSH receive buffer and the TCP receive buffer. OpenSSH has imposed a maximum receive buffer size of 2MB (which is a step up from the 64KB it used to be). This ends up being drastically undersized for HPN purposes. HPN-SSH was developed to dynamically grow the SSH buffer with the TCP receive buffer thereby removing a significant performance bottleneck. HPN-SSH also implements a ‘NULL cipher switch’. This allows SSH to switch to passing data in the clear but only *after* fully encrypted authentication takes place. This drastically reduces load on the CPU at both ends of the connection which eliminates another potential bottleneck. HPN-SSH maintains the message authentication cipher in order to protect against data corruption in transit. Lastly, standard SSH is highly linear in its execution and, as such, the process ends up being bound to a single core. This can result in an underutilization of available resources when encryption is required. HPN-SSH developed a multithreaded AES-CTR cipher that separates the key generation process from the rest of the dataflow. So when full security is required the load can be balanced across multiple CPU cores. This helps prevent the SSH process form being CPU bound.
Ideally users should have access to *both* GridFTP and HPN-SSH. If users cannot make use of GridFTP they should be strongly encouraged to use HPN-SSH. This being said GridFTP and HPN-SSH are not, by any means, the only data transfer tools available to users. Several organizations have developed transfer tools specific to the needs of their community. Examples would include GeneTorrent, DistCp,

## Slide 17: Tying it all together
Pay attention to the basics
  High latency is a major determinant of TCP behaviour
  Loss is unavoidable but can be minimized
  BDP must inform TCP options
Know your path
  Metrics and measurements are critical to providing rapid response to problems
Work with your users
  Provide the best possible tools
  Educate them and your front line support staff

## Slide 18: Questions?
Web10g:
  www.web10g.org
HPN-SSH:
  www.psc.edu/networking/projects/hpn-ssh
rapier@psc.edu
Notes: A valuable resource on tuning systems and networks for high performance operations can be found at http://fasterdata.es.net/
Perfsonar information can be found at http://www.perfsonar.net
HPN-SSH is found at http://www.psc.edu/networking/projects/hpn-ssh and http://sourceforge.net/projects/hpnssh
GridFTP, part of the Globus toolkit, is available from http://toolkit.globus.org/toolkit/